## Slide 1: Methods for Mounting LCD Displays
By John Khalaf
5-23-2016

## Slide 2
Modules have 3 mounting styles: Side Screws, Front Holes, No Holes
Side
Screws
Front
Holes
No Holes

## Slide 3
Disclaimer:
The methods shown in this presentation are for illustrative purposes only.
Your actual methods may be different.

## Slide 4
Side Screws Mounting
Bracket
Bezel
Seal
Displays should be supported in the center to prevent bowing. (Shown here is a bracket with foam against the back of the display.)
Attach bracket to customer housing
Two typical screw threads (depends on display):
M2 x 2.5mm depth MAX.
Torque is 2.0kgf cm Or
M3 x 3.9mm depth MAX.
Torque is 0.35Nm

## Slide 5
Front Holes Mounting
Front
Holes
Bezel
Seal
Displays should be supported in the center to prevent bowing. (Shown here is a bracket with foam against the back of the display.)
Stud and Nut

## Slide 6
No Holes Mounting
No Holes
Bracket provides full support to the Display edges
Bezel
Seal